## Slide 1
2019.07.31
Epileptic Seizure Detection using Deep Convolutional Autoencoder
LEEYEONSU

## Slide 2
EEG Spectral Feature Based Seizure Prediction using an Efficient Sparse Classifier
  Ahmed M. Abdelhameed
  2018 IEEE
Index

## Slide 3
Introduction
Proposed method
  Dataset
  1D Convolutional Autoencoder
  Neural network based classifiers
    Multilayer Perceptron
    LSTM
    Bidirectional LSTM
  Training and Experimental Results
    Data selection
    Convolutional autoencoder training
    Classifiers training
Results
Index

## Slide 4
Dataset
  CHB-MIT
  17 children
    78 seizures
    647hours of recording
  Sampling rate : 256Hz/sec
PROPOSED ALGORITHM
Window Based Signal Processing
  Segment : 4sec
    Overlap : 50%
  Seizure prediction : every 2sec

## Slide 5
Feature extraction
  Feature : 8 sub-bands
    Theta (4-8Hz)
    Alpha (8-13Hz)
    Beta (13-30Hz)
    Gamma1 (30-50Hz)
    Gamma2 (50-70Hz)
    Gamma3 (70-90Hz)
    Gamma4 (90-110Hz)
    Gamma5 (110-128Hz)
PROPOSED ALGORITHM

## Slide 6
Feature extraction
  Absolute Spectral Power
    Power of the signal in that particular frequency band
  Relative Spectral Power
    Ratio of power of the signal in that frequency band to the total power of the signal considering all the frequency bands
    RSP = BSP / TSP
      BSP(Band Spectral Power), TSP(Total Spectral Power)
  Spectral Power Ratio
    Between two bands is the ratio of spectral powers in those frequency bands
  Major problem
    Spectral power fluctuates not only in the preictal period but also in the inter-ictal period (decreases reliability to predict)
  Overcoming problem
    By considering spectral power ratios
      More indicative of an upcoming ictal events
PROPOSED ALGORITHM

## Slide 7
Feature Selection
  To reduce this feature set to optimum level ,
    Need to select features that contribute the most to seizure prediction
    Method
      Sparse feature selection
        Sparse Bayesian Multinomial Logistic Regression(SBMLR) technique (NIPS 2007)
        a-posteriori estimate of the probability that a pattern belongs to each of Disjoint classes
        Regularization parameter is used to check if it is below a threshold or not.
          Regularization parameter = The value of the gradient of this function
PROPOSED ALGORITHM
Features selected for Classification
4
31
42
< SELECTED FEATURES AFTER FEATURE SELECTION STAGE >

## Slide 8
Classification
  Sparse classifier (machine learning)
    Classification
      inter-ictal
      Pre-ictal
  For linearly non-separable data
    Used Sparse kernel function
      Make the data can be linearly separable
  Algorithm
    SRC ( Sparse Representation Classifier)
    KSRC ( Kernel Sparse Representation Classifier)
PROPOSED ALGORITHM
Notes: Sparse kernel function
  Implementation of Sparse Representation Classifier(SRC) to heartbeat biometrics
  Kernel = 연립일차방정식

## Slide 9
Classification
  SRC (Sparse Representation Classifier)
    Consider a data as a linearly separable
    Consider a data as a linearly non-separable
      Sparse kernel function is used to map the data in to higher dimension
        The data can be considered linearly separable
  =
    = signal to predict
    = coefficient matrix
    = training set
  - =
    = error value
      Minimum error
PROPOSED ALGORITHM
Notes: Sparse kernel function
  Implementation of Sparse Representation Classifier(SRC) to heartbeat biometrics

## Slide 10
Evaluated on Matlab2013 software
  Preictal period
    Between a preictal state has been identified & actually ictal happens
  Performance measurement
    Sensitivity = TP / ( TP + FN ) * 100
    False Positive Rate ( FPR ) = FP / ( FP + TN )
Results
< TABLE OF CONFUSION OF PROPOSED METHOD >
< PERFORMANCE PARAMETERS OF PROPOSED METHOD >
measure | sensitivity | specificity | FPR
 | 82.98% | 89.24% | 0.107
?
?

## Slide 11
  Backup Slides

## Slide 12
LITERATURE SURVEY
Related work
  Adaboost
  Adaptive Neuro Fuzzy Inference System
  Spike rate as the feature
  Spatial and temporal covariance matrix between different EEG channels
  Spectral power of various EEG bands (SVM for classification)
  HPD(Henze Penrose Divergence) - the factor to decide the reliability of a feature
  Cross correlation coefficients between different EEG electrodes
  Phase correlation between different EEG channels
Proposed method
  Efficient sparse classifier for preictal event identification

## Slide 13
Sparse feature selection
  SBMLR
PROPOSED ALGORITHM

## Slide 14
Kernel function
  원점을 중심으로 대칭이며 적분값이 1 인 양의 함수로 정의할 수 있습니다.